## Slide 1
Energy Storage For Mechatronic Energy
Harvesting System
Nikolaos Chrysogelos

## Slide 2
Storage Unit Optimization
Inductor Selection
Hardware Implementation
Control Scheme
Experimental results
Conclusions and Outlook

## Slide 3
Overview of the System

## Slide 4
Overview of the System
Harvester

## Slide 5
Overview of the System
Harvester
Pulsed Load

## Slide 6
Energy Storage Unit
Overview of the System
Harvester
Pulsed Load

## Slide 7
Topology of the Storage System

## Slide 8
 | Price (CHF) | C (F) | (V) | (mΩ) | Volume (l)
EPCOS (TDK) | 16.00 | 1 μF | 500 V | 12 mΩ | 
EPCOS (TDK) | 89.00 | 20μF | 500 V | 8 mΩ | 
 | Price (CHF) | C (F) |  |  | Volume (l)
EPCOS (TDK) | 16.00 | 1 μF | 500 V | 12 mΩ | 
EPCOS (TDK) | 89.00 | 20μF | 500 V | 8 mΩ | 
 | Price (CHF) | C (F) | (V) | (mΩ) | Volume (l)
Nichicon | 268 | 2.2 F | 10 V | 5 mΩ | 2
Vishay | 192.5 | 1 F | 25 V | 5 mΩ | 1.4
 | Price (CHF) | C (F) |  |  | Volume (l)
Nichicon | 268 | 2.2 F | 10 V | 5 mΩ | 2
Vishay | 192.5 | 1 F | 25 V | 5 mΩ | 1.4
Ceralink & ELCO
Low Energy Density (~0.3kJ/l)
Large Volume
Expensive
Low η(%)
Topology of the Storage System

## Slide 9
 | Price (CHF) | C (F) | (V) | (mΩ) | Volume (l)
EPCOS (TDK) | 16.00 | 1 μF | 500 V | 12 mΩ | 
EPCOS (TDK) | 89.00 | 20μF | 500 V | 8 mΩ | 
 | Price (CHF) | C (F) |  |  | Volume (l)
EPCOS (TDK) | 16.00 | 1 μF | 500 V | 12 mΩ | 
EPCOS (TDK) | 89.00 | 20μF | 500 V | 8 mΩ | 
 | Price (CHF) | C (F) | (V) | (mΩ) | Volume (l)
Nichicon | 268 | 2.2 F | 10 V | 5 mΩ | 2
Vishay | 192.5 | 1 F | 25 V | 5 mΩ | 1.4
 | Price (CHF) | C (F) |  |  | Volume (l)
Nichicon | 268 | 2.2 F | 10 V | 5 mΩ | 2
Vishay | 192.5 | 1 F | 25 V | 5 mΩ | 1.4
 | Price (CHF) | C (F) | (V) | (mΩ) | Volume (l)
Eaton Bussmann | 6.84 | 35 F | 2.7 V | 20 mΩ | 
Eaton Bussmann | 7.09 | 60 F | 2.7 V | 18 mΩ | 
 | Price (CHF) | C (F) |  |  | Volume (l)
Eaton Bussmann | 6.84 | 35 F | 2.7 V | 20 mΩ | 
Eaton Bussmann | 7.09 | 60 F | 2.7 V | 18 mΩ | 
 | Price (CHF) | Capacity (mAh) | (V) | (Ω) | Volume (l)
ST Microelectronics | 30 | 0.7 mAh | 3.9 V | 100 Ω | 
Infinite Power Sol. | 53.46 | 2.2 mAh | 4.1 V | 20 mΩ | 
 | Price (CHF) | Capacity (mAh) |  |  | Volume (l)
ST Microelectronics | 30 | 0.7 mAh | 3.9 V | 100 Ω | 
Infinite Power Sol. | 53.46 | 2.2 mAh | 4.1 V | 20 mΩ | 
Ceralink & ELCO
Thin Film Batterries
Low Energy Density (~0.3kJ/l)
Large Volume
Expensive
Low η(%)
Large Energy Density (~15kJ/l)
Cheap
Great Volumetric Energy density
H η(%)
Super Capacitors
Topology of the Storage System

## Slide 10
Design of the Storage System
Design

## Slide 11
Optimization
Design of the Storage System
Cost (CHF)
Volume (l)
Efficiency (%)
Design

## Slide 12
Super Capacitor Optimization

## Slide 13
Super Capacitor Optimization
Nominal Case | Worst Case
F | F
J | J
s | s
Nominal Case | Worst Case
 | Eaton Bussmann HV1245-2R7356-R
Price (CHF) | 6.84CHF
C (F) | 35 F
Voltage (V) | 2.7 V
mΩ | 20 mΩ
Volume (l) | 
 | Eaton Bussmann HV1245-2R7356-R
Price (CHF) | 
C (F) | 35 F
Voltage (V) | 2.7 V
 | 20 mΩ
Volume (l) | 
Nr | 9
Price (CHF) | 6.84 9 = 61.56 CHF
Voltage (V) | 2.7 V9 = 24.3 V
Volume (l) | 0.05 l
Nr | 9
Price (CHF) | 
Voltage (V) | 
Volume (l) | 0.05 l

## Slide 14
Requirements
Operation in CCM
Storage Unit
Bus
Analysis of the Energy Storage Unit

## Slide 15
Inductor Optimization (1)
Inductor Design

## Slide 16
Inductor Optimization (1)
Inductor Design
Efficiency of the ESU

## Slide 17
Inductor Optimization (1)
Inductor Design
Efficiency of the ESU

## Slide 18
Must achieve correct inductance
Keep the losses low
Inductor size as small as possible without saturating the core
Requirements
Commercial Custom cores
GeckoMagnetics simulations
Commercial Fixed value Inductors
Inductor Optimization (2)

## Slide 19
Commercial Cores used: Digikey and Rotima
Custom Cores
Must achieve correct inductance
Keep the losses low
Inductor size as small as possible without saturating the core
Requirements
GeckoMagnetics
RM 14 0.15mm | ETD 54/28/19
290 μΗ | 294.59 μΗ
N87+ | N87+
AWG12 | AWG12
15 turns | 14 turns
9.2 mΩ | 9.4 mΩ
0.08 l | 0.04 l
7 CHF | 11.2 CHF
Selected Inductor
 | M8379-ND
Price CHF) | 7.65 CHF
Material | Ferrite
L (μH) | 220 μH
(A) | 7.4 A
(mΩ) | 50 mΩ
Volume (l) | 0.03 l
 | M8379-ND
Price CHF) | 7.65 CHF
Material | Ferrite
L (μH) | 220 μH
 | 7.4 A
 | 50 mΩ
Volume (l) | 0.03 l
Commercial Custom cores
GeckoMagnetics simulations
Commercial Fixed value Inductors
Inductor Optimization (2)

## Slide 20
Hardware Implementation
Component | Nr | Volume (l)
Eaton Bussmann (SuperCap) | × 9 | 0.05
M8379-ND (Inductor) | × 1 | 0.03
Cap 1210 X7R (Capacitor) | × 4 | 
Res 1206 (Resistor) | × 9 | 
Component | Nr | Volume (l)
Eaton Bussmann (SuperCap) | × 9 | 0.05
M8379-ND (Inductor) | × 1 | 0.03
Cap 1210 X7R (Capacitor) | × 4 | 
Res 1206 (Resistor) | × 9 | 

## Slide 21
Hardware Implementation
0.18 liter
Volume
Component | Nr | Volume (l)
Eaton Bussmann (SuperCap) | × 9 | 0.05
M8379-ND (Inductor) | × 1 | 0.03
Cap 1210 X7R (Capacitor) | × 4 | 
Res 1206 (Resistor) | × 9 | 
Component | Nr | Volume (l)
Eaton Bussmann (SuperCap) | × 9 | 0.05
M8379-ND (Inductor) | × 1 | 0.03
Cap 1210 X7R (Capacitor) | × 4 | 
Res 1206 (Resistor) | × 9 | 

## Slide 22
Control Scheme
Efficient storage of the power provided by the harvester
Deliver required power to the load
Requirements
Notes: build a circuit that automatically adjusts the duty cycle as necessary, to obtain the specified output voltage with high accuracy, regardless of disturbances or component tolerances.

## Slide 23
Control Scheme
Efficient storage of the power provided by the harvester
Deliver required power to the load
Requirements
Use of a closed-loop control scheme (negative feedback)
Adjust duty cycle to obtain desired output voltage regardless Load variations and Storage Unit voltage
Solution
Notes: build a circuit that automatically adjusts the duty cycle as necessary, to obtain the specified output voltage with high accuracy, regardless of disturbances or component tolerances.

## Slide 24
Manual Tuning of PI terms using Ziegler-Nichols technique,
PI Control
Input
PWM signal to Q1, Q2
Adjusting input control signal so that bus voltage stable
Converter
Reduces steady-state error
Improve the rejection of low frequency disturbances
Special attention must be given to the stability of the system
PI Control
PI Controller
Notes: - PI control attempts to drive the error to zero (Vref=Vout)
- It is performed by setting the I (integral) gains to zero and increase the Kp gain until it reaches the value Ku, at which the output of the control loop has stable and consistent oscillations. Ku and the oscillation period Tu are used to set the P and I gains

## Slide 25
PI Control Simulations – Charging Stage
(%) | 78%
 | 5.5 W
 | 3 W
 | 1.25 W
 | 0.7 V
 | 78%
 | 5.5 W
 | 3 W
 | 1.25 W
 | 0.7 V
(%) | 85%
 | 6 W
 | 4 W
 | 1.3 W
 | 0.4 V
 | 85%
 | 6 W
 | 4 W
 | 1.3 W
 | 0.4 V
Charging
Charging
(%) | ≥ 78%
 | 311 s
 | 5 W
 | ≤ 4 W
 | 1.3 W
 | ≤ 1 V
 | ≥ 78%
 | 311 s
 | 5 W
 | ≤ 4 W
 | 1.3 W
 | ≤ 1 V
Summary
Notes: The harvester may be simulated as a constant voltage source of 26.4V output and 11.43 internal
resistance.
As was explained in the rst chapter, the storage unit in order to be fully charged needs
approximately 300 seconds which is not possible to be simulated. Thus two gures are displayed;
the rst one is from the rst 10 seconds and at the second one Vsc was initialized at 22V.
So, in
the beginning a large amount of power is consumed in the internal ESR of each cell but as the
voltage across it continues to increase, it is used for the charging of the storage unit.
Finally, it is noted that the optimum way to charge the Supercapacitors is by providing maximum
power transfer from the harvester to the ESU. This may happen by applying almost constant
current with an exponential increasing voltage until it reaches 24V point at which the current is
falling to keep the absorbed power constant.

## Slide 26
PI Control Simulations – Discharging Stage
(%) | 95 %
 | 38 W
 | 36.2 W
 | ≤ 2.4 V
 | 95 %
 | 38 W
 | 36.2 W
 | ≤ 2.4 V
(%) | 95%
 | 26.4 V
 | 2.4 V
 | 300μs
 | 2.3 ms
 | 95%
 | 26.4 V
 | 2.4 V
 | 300μs
 | 2.3 ms
Discharging t=1s
Discharging
(%) | 95%
 | 22 s
 | ≤ 38 W
 | ≤ 36.5 W
 | ≤ 2.4 V
 | 95%
 | 22 s
 | ≤ 38 W
 | ≤ 36.5 W
 | ≤ 2.4 V
Summary
Notes: The harvester may be simulated as a constant voltage source of 26.4V output and 11.43 internal
resistance.
As was explained in the rst chapter, the storage unit in order to be fully charged needs
approximately 300 seconds which is not possible to be simulated. Thus two gures are displayed;
the rst one is from the rst 10 seconds and at the second one Vsc was initialized at 22V.
So, in
the beginning a large amount of power is consumed in the internal ESR of each cell but as the
voltage across it continues to increase, it is used for the charging of the storage unit.
Finally, it is noted that the optimum way to charge the Supercapacitors is by providing maximum
power transfer from the harvester to the ESU. This may happen by applying almost constant
current with an exponential increasing voltage until it reaches 24V point at which the current is
falling to keep the absorbed power constant.

## Slide 27
Software Implementation
Used μC: ATMEGA88PA
Sampling period = 4kHz
Reading of the ADC values = 128 kHz
Characteristics
Integral windup ( term accumulates a significant error)
If it reaches a max value re-initialize
ADC inputs read large spikes
Keep the last values and average them
Float numbers result in slow running times
Use of integer numbers
Fast PWM signal of 64 kHz
Limitations

## Slide 28
Experimental Results
 | 25.4 V
 | 0.2 A
 | 1.8V 9 = 16.2 V
 | 0.185 A
 | < 1 V
 | 25.4 V
 | 0.2 A
 | 0.185 A
 | < 1 V
 | 75%
 | 75%
Re-tuning of PI terms
Keep bus voltage stable
Charging Efficiency,
 | 78%
 | 78%
Experimental
Simulations

## Slide 29
Conclusions
Optimum Storage System and inductor design and implementation in terms of cost (CHF), Volume (l) and Efficiency (%) was designed
PI controller achieved to keep stable regardless load and voltage variations
Verified by simulations (GeckoCircuits) and experiments
Summary

## Slide 30
Outlook
  Experimental setup for the discharging cycle
Improved PI control scheme
  Cascaded voltage and current loop control
  Improved Evaluation of PI terms by using different values for
  and
  Optimization of algorithm for integer numbers
Future work

## Slide 31
Discussion

## Slide 32
Super Capacitors
Balancing SuperCapacitors
Impact on generator

## Slide 33
Inductor Design
1. Sizing a toroidal Core
In case of exceed of
Choose larger/different Core/Material
Operate in lower current
Increase air gap
Increase number of turns
2. Check
3. Number of Turns
4. Winding type
5. Define Power losses

## Slide 34
Ferrite Cores
Rotima Cores
 | O.D. (mm) | V (cm3) | Ac x Aw (cm4) | Nmin | B (T)
MP1603MP | 15.79 | 0.345 | 0.055 | 104.7 | 1.11
MP1710MP | 17.47 | 0.938 | 0.23 | 75.6 | 0.69
MP2010MP | 19.93 | 1.538 | 0.348 | 63.9 | 0.54
MP2310MP | 22.96 | 2.382 | 0.494 | 56.1 | 0.44
MP2510MP | 25.55 | 1.888 | 0.725 | 78.8 | 0.49
MP3310MP | 32.43 | 5.336 | 1.21 | 50.1 | 0.30
MP3510MP | 34.92 | 5.577 | 1.77 | 55.5 | 0.29
Price (CHF) | O.D. (mm) | V (cm3) | Ac x Aw (cm4) | Nmin | B (T) | (mm)
8.61 | 51.80 | 45 | 13.83 | 8.2 | 0.65 | 2.07
15.13 | 65.30 | 89 | 34.69 | 4.9 | 0.70 | 1.33
3.26 | 31.00 | 12 | 2.18 | 4.8 | 2.84 | 5.28
3.37 | 35.50 | 13 | 2.72 | 7.4 | 1.71 | 4.93
3.82 | 37.50 | 18 | 3.98 | 4.7 | 2.33 | 4.24
11.66 | 60.10 | 53 | 19.92 | 7.5 | 0.92 | 2.67
3.47 | 37.50 | 18 | 3.98 | 6.1 | 1.80 | 4.24
10.64 | 58.30 | 47 | 19.92 | 7.5 | 0.92 | 2.67
Price (CHF) | O.D. (mm) | V (cm3) | Ac x Aw (cm4) | Nmin | B (T) | 
8.61 | 51.80 | 45 | 13.83 | 8.2 | 0.65 | 2.07
15.13 | 65.30 | 89 | 34.69 | 4.9 | 0.70 | 1.33
3.26 | 31.00 | 12 | 2.18 | 4.8 | 2.84 | 5.28
3.37 | 35.50 | 13 | 2.72 | 7.4 | 1.71 | 4.93
3.82 | 37.50 | 18 | 3.98 | 4.7 | 2.33 | 4.24
11.66 | 60.10 | 53 | 19.92 | 7.5 | 0.92 | 2.67
3.47 | 37.50 | 18 | 3.98 | 6.1 | 1.80 | 4.24
10.64 | 58.30 | 47 | 19.92 | 7.5 | 0.92 | 2.67
Inductor Results

## Slide 35
Mosfet Losses
Mosfet losses | 
Gate Losses | 
Turn-on Losses | 
Turn-off Losses | 
Coss Losses | 
Conduction Losses | 
Mosfet losses | 
Gate Losses | 
Turn-on Losses | 
Turn-off Losses | 
Coss Losses | 
Conduction Losses | 

## Slide 36
Discharging Stage at t=1s
 | 26.4 V
η (%) | 95%
 | 2.4 V
 | 300μs
 | 2.3 ms
 | 26.4 V
η (%) | 95%
 | 2.4 V
 | 300μs
 | 2.3 ms
Discharging t=1s

## Slide 37
ADC Reading Problem